FA

INCLUDE the presenting author’s complete contact information i.e, name, company, address, country, and email.

ABSTRACT LIMIT IS 250 WORDS

Template

The enzymatic paper-on-a-chip concept: Towards the on-site organophosphate and carbamate pesticides detection in fruits and vegetables

Aristeidis Tsagkaris,1 Daniel Filippini,2 J.-Pablo Salvador,3,4 M.-Pilar Marco, 3,4 Jana Pulkrabova,1 and Jana Hajslova;1  

1University of Chemistry and Technology Prague, Department of Food Analysis and Nutrition, Faculty of Food and Biochemical Technology, University of Chemistry and Technology Prague, Technická 5, 166 28 Prague 6 – Dejvice,

Prague, Czech Republic; tsagkara@vscht.cz; 2 Optical Devices Laboratory, Department of Physics, Chemistry and Biology—IFM, Linköping University, S-58183 Linköping, Sweden; 3 Nanobiotechnology for diagnostics (Nb4D), Institute for Advanced Chemistry of Catalonia (IQAC) of the Spanish Council for Scientific Research (CSIC), Jordi Girona 18-26, 08034 Barcelona, Spain; 4 CIBER de Bioingeniería, Biomateriales y Nanomedicina (CIBER-BBN)

Lab-on-a-chip (LOC) devices is a concept of increasing popularity because it provides miniaturization, integrated sample handling and low-cost measurement. Although the determination of organophosphate and carbamate pesticides requires expensive and time-consuming chromatographic methods, rapid screening can be achieved based on the principle that organophosphates and carbamates inhibit acetylcholinesterase (AChE). In-vitro, AChE can hydrolyze certain colorless substrates to color products. However in the presence of an inhibitor, AChE is inhibited dependently on a pesticide concentration and this inhibition can be correlated to a color intensity decrease. To this end, we developed an interdisciplinary analytical platform for organophosphates and carbamates detection. To begin with, AChE was physically adsorbed on Whatman paper.  Then, two AChE strips were incorporated in a prototype LOC creating a so called enzymatic paper-on-a-chip (EPOC) device. The EPOC device provided integrated samples and substrates loading using silicon tubes as a pumping element eliminating the pipetting need. To monitor the color development on AChE strips, the EPOC device was placed in an in-house 3D-printed smartphone reader. Paper assay images were captured using the OpenCamera application and image data processing was performed in MatLab. Finally, the developed platform was successfully used to quantitatively detect carbofuran in apple extracts at sub-ppm level. Despite being a restricted pesticide in the EU, carbofuran was recorded among the pesticides with frequent MRL exceedances in the latest EFSA report indicating the need for rapid screening methods. All in all, this fast, simple and cost-effective approach can be a paradigm shift towards the on-site chemical residues detection.

Acknowledgement

This project has received funding from the European Union’s Horizon 2020 research and innovation program under the Marie Sklodowska-Curie grant agreement No 720325, FoodSmatrphone

# Text boxes

Please complete the abstract using the template below by replacing the example given with your own submission.

Do not change the spacing (single), font (10 point Calibri), margins, or justification (left).  ABSTRACT LIMIT IS 250 WORDS.  Use bold text for the title (2 lines maximum).

List the authors separated by commas with superscript numbers to denote institutions if more than one.  Underline the name of the presenting author.  List the presenting author’s institute name in bold text and address, including country followed by a semicolon; then email address.  Add additional institute information as needed, then skip a line and enter your text.