Title: Optimisation of N application in a shallow irrigated soil bearing a maize crop.

Short title: N application rate in a shallow irrigated soil

J.A.Díez1,*, A.Tarquis2, M.C.Cartagena2 & A.Vallejo2

1Environmental Sciences Centre CSIC, Serrano 115,  28006 Madrid, Spain; Phone +34 917452500

fax: +34 915640800).

2Escuela Técnica Superior de Ingenieros Agrónomos, Universidad Politécnica de Madrid, Ciudad 00Universitaria. 28040 Madrid, Spain.

*Corresponding author: jadiez@ccma.csic.es ;

7 Tables

2 Figures

Optimisation of N application in a shallow irrigated soil bearing a maize crop.

J.A.Díez1,*, A.Tarquis2, M.C.Cartagena2 & A.Vallejo2

1Environmental Sciences Centre CSIC, Serrano 115,  28006 Madrid, Spain; 2Escuela Técnica Superior de Ingenieros Agrónomos, Universidad Politécnica de Madrid, Ciudad Universitaria. 28040 Madrid, Spain. *Corresponding author . E-mail: jadiez@ccma.csic.es ; fax: +34 915640800)

Abstract

A methodology to evaluate the net N mineralised in shallow soils, based on N balances in non-fertilized plots, is proposed. During 1999, 2000 and 2001, the N mineralised in a maize crop irrigated in Central  Spain was: 73.3,  55.4  and  60.5 kg N ha-1, respectively. The relationship observed in this experiment between EUF-Norg and the nitrogen mineralised during the three crops (mean value), was  1 mg  EUF-Norg 100 g-1 soil = 30 kg N ha-1. This calibration was applied to EUF-Norg values obtained from soil samples analysed before the sowing of the crop. This values, together with the mineral N, were used to estimate the N available and consequently the optimised nitrogen rate. N optimised rates for the maize crop, were 150 and 130 kg N ha-1, in 2000 and 2001, respectively. The losses of nitrate by leaching were lower with the optimised rate of nitrogen (NO) than with the conventional rate (NC) of 300 kg N ha-1. However, in spite of the difference in N applied, no effect was observed in the grain yield in any treatments.

##### Key words : shallow soils, optimal nitrogen rate, EUF, N balance.

##### Resumen

Optimización de la dosis de nitrógeno en suelos poco profundos irrigados, bajo cultivo de maiz

Se propone una metodología para evaluar el nitrógeno mineralizado en suelos petrocalcicos poco profundos, basada en los balances de nitrógeno en parcelas no fertilizadas. Durante los años 1999, 2000 y 2001 el N mineralizado en un cultivo de maíz irrigado en la zona Centro de España fue  73.3, 55.4 y 60.5 kg N/ha-1, respectivamente. La relación observada en este experimento, entre EUF-Norg y el N mineralizado durante los tres periodos de cultivo (valores medios), fue 1 mg  EUF-Norg 100 g-1 soil = 30 kg N ha-1. Esta calibración se aplicó a los valores de EUF-Norg correspondientes a las  muestras de suelo tomadas antes del cultivo. Con estos valores junto con el N mineral del suelo se determinó en N asimilable y la dosis optimizada de N. Las dosis de N optimizado (NO) aplicadas fueron 150 y 130 kg N ha-1, en 2000 y 2001, respectivamente. El nitrato perdido por lixiviación fue mas bajo con la dosis  optimizada de nitrógeno (NO) comparada con la dosis convencional (NC) de 300 kg N ha-1. Sin embargo, a pesar de las diferencias en las dosis de N aplicadas en ambos tratamientos, no se obsevó ningun efecto sobre la producción de grano.

##### Palabras clave: suelos poco profundos, dosis optima, nitrógeno, EUF, balance de N.

##### Introduction

In irrigated soils, mineralization of soil organic N during the crop season must be taken into account in order to know the N available, and consequently, to improve fertilizer efficiency. In these soils, net N mineralization is often very high in summer, due to soil conditions (moisture and temperature). Even in soils with low organic matter content, net N mineralised can be high. Sánchez et al. (1998) measured 165 kg N ha-1 during a maize growing season in an irrigated sandy loam soil in Mediterranean climate. Quantification of net N mineralised under field conditions is difficult, although methods based on mineral N balance during the growing season for various consecutive years have given useful results. The balance method used by Sánchez et al. (1998) was used to measure nitrate leaching, N mineral exchange in the soil during the crop period and N uptake by the crop. However, when soils are stony and/or shallow, the methodology must be revised because the high amount of stones complicates nitrate leaching measurements. These soils occupy large areas, especially in  Mediterranean countries, where there is a petrocalcic horizon close to the surface. For such soils, net N mineralization has still not been determined.

Various soil tests have been proposed to estimate N available (Nav) for the crop, such as incubation (Stanford 1982), or soil extraction methods (Khan  et al. 2001; Mengel 1991; Németh 1979) as the extraction with CaCl2 0.01M  (Houba et al.1986). It is necessary to arrange a soil test to estimate the labile N organic fraction, which supplies N to the plant through mineralization (Khan et al. 2001; Mengel 1991). The electro-ultrafiltration (EUF) extraction method proposed by Németh (1979) allows reliable information of the different forms of N in the soil. By applying an electric field, inorganic ions (NO3- and NH4+) and organic N compounds (mainly peptides and proteins) are desorbed from soil colloids. Satisfactory relationships between analyses in EUF-obtained extracts (Total EUF-N in extracts, EUF-NO3-, EUF-NH4+ and EUF-Norg) and N uptake by the plant (Fürstenfeld & Németh 1984; Poletschny & Fabian 1989; Wiklicky et al. 1983; Wiklicky & Németh 1981; Ziegler et al. 1992) have been reported. Wiklicky & Németh (1981) have proposed to estimate available N  with the equation:

Nav =  (EUF-NO3-) x a + (EUF-Norg) x b  			(1(

EUF-NH4+  was included in EUF-Norg fraction to calculate the N available. Nav is available N for the crop in kg N ha-1, a and b are parameters to obtain the NO3- and Norg  mineralized in the soil, respectively. A relationship between  b and N mineralization, has been observed (Nemeth, 1979). Wiklicky & Németh (1981) using a ‘b’ value of 50 for a sugar beet crop (Beta vulgaris) in Austria, growed on loess soils and with a typical centro-European climate. However, the results of the numerous field experiments performed during the last decades show that the N mineralised, used to calibrate the extractable Norg (b parameter), was not the same for different growing seasons, geographical regions, management practices and types of soil. Theoretically, for each combination of these factors, separate calibrations would be necessary (Appel and Mengel, 1998). Nevertheless, when conditions are known, such as a maize crop, with a hot seasonal period of cultivation, irrigated and in a specific type of soil, these calibrations can be very useful.

The main aim of this study was to assess the mineralised nitrogen in calcareous soils with a petrocalcic horizon at a 50 cm depth in a Mediterranean-climate, based on the N balance in non-fertilized plots under field conditions. Another objective was to assess the optimal rate of nitrogen by means of the N available of the soil, calculated from the addition of N mineralised and N mineral.

### Materials and methods

Soil Characteristics

Experiments were carried out in an irrigated maize crop at Las Tiesas Field Station (5 km east of Albacete, Spain) during 1999, 2000 and 2001. The soil (Calcic Xerosol) is shallow  and has a petrocalcic horizon. Each experimental year, in March, soil from Control plots was sampled to characterize the soil and to establish  the N mineralised by means of  N the balance. Fresh soil samples were air-dried and sieved at 2 mm. Soil characteristics are shown in Table 1.  The pH of the soil was basic, with a high carbonate level and a bulk density of 1.30.  It has a sandy loam texture. The depth of the soil was 50-55 cm, below which a 1-3 m thick petrocalcic horizon appeared.  This horizon gave rise to a high degree of soil stoniness (20 – 30%).

Table 1. Physicochemical properties of soil at the start of the experiment in ploughed soil layer. Mean and SD of plots.

| pH (H2O) | 7.7 ± 0.1 |
| --- | --- |
| Bulk density (Tm m-3) | 1.30 ±0.02 |
| C (g kg-1 ) | 8.70 ±003 |
| Organic matter (g kg-1) | 15.0 ± 1.2 |
| Carbonate (g kg-1 ) | 350 ± 14.0 |
| Clay (%) | 38 |
| Silt (%) | 42 |
| Sand (%) | 20 |

Experimental Design

Nine 100 m2 plots were randomly distributed in blocks with three treatments and three replications. The treatments were: non-fertilized control (C), conventional N rate (NC, 300 kg N ha-1) in three splits of 100 kg N ha-1 (NH4NO3 33.5% N)  and an optimised dose (NO) as a single application  40 days after sowing, with the same fertiliser. The conventional rate represents the mean  rate applied by farmers in the region.  The optimised dose applied was calculated though the EUF technique [1 eq.]. A previous experiment was made in 1999 to determine N mineralised in plots without fertiliser during a maize crop (from 20th April to 30th October) with irrigation. During the three experimental  years, the mineralised N was determined from the N balance in the non-fertilised plots. ‘b’ parameter of eq (1(  was then recalibrated for the next experimental year with mineralised N.

Crops and irrigation management

Maize cv Pregia was sown to a density of 86580 seeds/ha (0.165 x 0.70 m) in the stubble of the previous year's crop on  April 25 in 1999, May 8 in 2000 and April 30 in 2001. The seedbed in all plots was prepared with calcium superphosphate and potassium sulphate fertilizer (200 kg P2O5 ha-1 and 100 kg K2O ha-1). A combination of 48% Alachlor (3 l ha-1), 33% Pendimetaline (3 l ha-1) and 24% Bromoxynil (0.75 l ha-1) was applied before emergence for weed control. Methylchloropyriphites (48%) and Cypermetrine (10%) were supplied in irrigation water (dissolved in 70 m-3 ha-1) to prevent maize borer.  The crop was harvested in October.

A year before the beginning of the experiment, a system for monitoring soil water-content in real time, using semipermanent multisensor capacitance probes (EnviroSCAN, Sentek Pty Ltd, South Australia) was installed (Buss 1993). Drainage was calculated as follows:

D = R + I – ET ( (S  			[2]

where R is rainfall (mm), I is irrigation (mm), ET  evapotranspiration (mm) and ΔS  changes in soil water (mm) from 0 to 50 cm depth. Four of the nine experimental plots were provided with EnviroSCAN probes (50 mm interior diameter) of 50 cm depth. The sensors were situated inside the probes at 5, 15, 35 and 45 cm depth (Fig 1). The frequency signal (FS) from the apparatus was converted into a measure of the volumetric moisture content ((v) using the calibration equation of Paltineanu and Starr (1997) in a soil with similar texture. Measures were taken every hour during the cultivation period of each year. A data logger recorded the data. Drainage was calculated from the  water content curves obtained by EnviroSCAN (Sentek, 2000) data during the crop period. The use of the EnviroSCAN system made unnecessary the installation of tensiometers to determine the direction of water-flux in the soil, because this information was obtained with the same system. For drainage calculation the decrease of water reserve curves (EnviroSCAN) corresponding to the sensors situated near the drainage zone (45 cm depth) were used.

Fig 1

Plots were watered periodically (9 irrigations in 1999, 10 irrigations in 2000 and 12 in 2001) depending on the evapotranspiration (ETc). The ETc (crop evapotranspiration) was estimated via the crop coefficient Kc using the Penman-Monteith model (de Juan et al. 1996) with data provided by a meteorological station situated inside experimental field. The Kc was 0.40 for the first 70 days.  Then, it increased to 1.20 until maturity (130 days), and ended at 0.70 at harvest. Table 2 shows the rainfall and irrigation data during the three years of the experiment. Water for irrigation came from the estate’s well. The nitrate concentration in irrigation water was lower than 3 mg L-1.

Methodology to determine NO3- leaching must be adapted to this type of soil. Three ceramic candles (tubes with 63 mm interior diameter) were installed in each plot at a 45 cm soil depth to obtain soil solution samples. It was necessary to prevent the contact between the ceramic and the petrocalcic horizon to assure the vacuum. Water samples from the ceramic candles were taken weekly and nitrate concentrations were determined. NO3-  leaching was calculated as the product of the drained water and nitrate concentration in the soil solution (Díez et al. 1996; Díez et al. 2000).

Soil Analysis

The EUF method was applied, following the program of Németh (1979). Samples were taken from the ploughed soil layer (0-30 cm) in March.  A 5 g representative sample of air-dried soil (< 1mm) was weighed and introduced in a EUF cell (Vogel S-724).

Soil pH was determined in water using a calomel glass electrode (ISO 10390, 1994).  Soil organic matter content was determined following the ISO 14235 (1998) method.  Carbonates were measured by gasometry (ISO 10693, 1995). Particle size distribution was measured using a Robinson pipette (ISO 11277, 1998).  Total N (Nt) in EUF extracts were determined by UV radiation digestion and subsequent oxidation with potassium persulphate in an alkaline medium (Díez 1988). The determination of N in the extracts was performed colorimetrically using a Technicon AAII Autoanalyzer (Technicon Hispania, Madrid) with N1-naphthylethylendiamine. A NH4+-N analysis was also performed using the same device but with nitroprussiate. EUF-Norg was estimated as the difference between EUF-N and EUF-(NO3- plus NH4+).

Nitrogen balance

N balance was calculated using the protocol of Sánchez et al. (1998):

Nmin =  (Ni – Nf) + Nleached + Ntaken up				[3]

where Nmin = mineralised N,  Ni= initial mineral N  and Nf = final mineral N

Initial and final refer to the soil nitrogen before sowing and after harvest, respectively. The soil profile was divided into two sections: 0-30 cm and 30-50 cm. In the first section, soil samples were taken at 15 cm for EUF extraction of Ninitial and Nfinal. NO3-, NH4+ and organic N were also determined.  The sample of the second section was taken from a depth of 40 cm. Samples were dried, passed through a 2 mm sieve and extracted with 2M KCl 1:5 solution/soil ratio; shaking time was 2 h. Samples were centrifuged and nitrate and ammonium were analysed (the organic material at this depth was very scarce).

The change in mineral N (ΔN) is the change observed between final N soil content (0-30 cm and 30-50 cm depth) and initial N in the soil.

ΔN = Nfinal - Ninitial

Nmin, Nleached and Ntaken up refer to the cultivation period. Denitrification and volatilisation not were considered as they are negligible in this Mediterranean climate in non-fertilised soils. (Arcara et al. 1998;  Sánchez et al. 2001).

N uptake (aboveground biomass) was measured in ten harvested plants, selected randomly from a 5 m strip of two adjacent rows in the middle of each plot. Samples were separated: stalk, leaves, bracts, cob and grain and oven-dried for 24 h at 60ºC and 2 h at 80ºC to determine dry matter (DM) content. Grain yield was calculated taking into account a standard grain moisture content of 14%. Nitrogen concentration was determined in plant fractions by the Kjeldahl method (AOAC 1990).  Samples were pre-treated with a solution of salicylic and sulphuric acids (Bremner 1965). Plant N uptake was calculated by multiplying fraction yields by their respective N concentrations.

With this information the ‘b’ parameter of equation [1] has been calculated by dividing  mineralised N (Nmin) by Norg extracted by EUF.

### Results

Cumulative drainage during the crop period was 158, 119 and 78 mm in 1999, 2000 and 2001, respectively (Table 2), representing 28.5, 15.1 and 9.6% of total amount of water applied. In 1999 the drainage was higher due to the rain was only 198 mm H2O. Under conventional irrigation practices, drainage usually exceeds 20% in this area (Román et al. 1996).

Table 2- Water balance during the experimental period (mm). Drainage was calculated by EnviroSCAN. (Sentek, 2000)

|  | 1999 | 2000 | 2001 |
| --- | --- | --- | --- |
| Rain | 198 | 18 | 66 |
| Irrigation | 554 | 765 | 690 |
| Drainage | 158 | 119 | 78 |
| ETc | 602 | 668 | 683 |

Nitrate concentrations were generally low (Table 3), especially in the control and NO treatments. The NC treatment showed higher nitrate levels due to the higher N doses applied. Consequently, nitrate leaching losses were low, probably as a consequence of the low soil water’s ion concentration, the good irrigation control achieved and the shallowness of the soil. Nitrate losses during 2000 together with 2001 were 4.2, 22.2  and 7.2 kg N ha-1 for Control, NC and NO respectively. Adjustment of fertiliser-N doses diminished the leaching losses.

Table 3.- Mean of nitrate concentration [NO3-N]  at 45 cm depth  and leached N during maize crop growth during years  1999, 2000 and 2001.

| Treatments | [NO3--N ] (mg L-1) | NO3- leached (kg N ha-1) | [NO3--N ] (mg L-1) | NO3- leached (kg N ha-1) | [NO3--N ] (mg L-1) | NO3- leached (kg N ha-1) |
| --- | --- | --- | --- | --- | --- | --- |
|  | 1999 | 2000 | 2001 |
| †C | 5.7 ± 5.2‡ | 3.2 | 4.8a ± 4.8 | 2.6 | 0.94a ± 1.2 | 1.65 |
| NC |  |  | 18.1b ± 16 | 7.9 | 17.0b ± 7.5 | 14.30 |
| NO |  |  | 6.6ab ± 6.6 | 5.5 | 1.1a ± 1.8 | 1.70 |

†C: control; NC: conventional nitrogen rate; NO: optimised nitrogen rate.

‡ Mean ± standard deviation. These data are based on 7 samplings in 1999, 7 samplings in 2000 and 11 samplings in 2001 with nine replicated extraction cups per fertiliser.

a,b For each column [NO3--N ], mean values followed by the same letter are not significantly different (P < 0.05, Duncan test).

The values of mineral N in the section 0-30 cm of soil were obtained by EUF method, while those from the 30-50 section were obtained through  an extraction with 2M KCl solution. Variations  of  mineral N (ΔN) for the maize were negative ( -22.1 in 1999, -43.91 kg N ha-1 in 2000 and -23.53 kg N ha-1 in 2001) (Table 4), suggesting that available N reserves decresaed in the soil profile throughout the growing cycle. This is mainly due to the removal of nitrogen by the maize, whereas leaching losses were small.

Table 4.- N balance in non-fertilised plots in maize during the crop.

| treatments | Depth (cm) | N mineral | ΣN (0-50) | ΔN=Nf-Ni |
| --- | --- | --- | --- | --- |
|  |  | (mg N 100g-1) | (kg N ha-1) |  |  |
| 1999 |
| Ni Ni | 0-30 | 1.35 | 52.6 | 73.4 | -32.5 |
|  | 30-50 | 0.80 | 20.8 |  |  |
| Nf Nf | 0-30 | 0.75 | 29.2 | 40.9 |  |
|  | 30-50 | 0.45 | 11.7 |  |  |
| 2000 |
| Ni Ni | 0-30 | a1.10±0.12 | 42.90 | 61.10 | -42.12 |
|  | 30-50 | b0.70±0.17 | 18.20 |  |  |
| Nf Nf | 0-30 | 0.32±0.07 | 12.48 | 18.98 |  |
|  | 30-50 | 0.25±0.05 | 6.50 |  |  |
| 2001 |
| Ni Ni | 0-30 | 0.92±0.08 | 35.88 | 51.48 | -23.53 |
|  | 30-50 | 0.60±0.09 | 15.60 |  |  |
| Nf Nf | 0-30 | 0.55±0.14 | 21.45 | 27.95 |  |
|  | 30-50 | 0.25±0.05 | 6.50 |  |  |

a 1 mg N 100g1 = 30 (cm depth) x 1.3  (bulk density)  kg ha-1

b 1 mg N 100g1 = 20 (cm depth) x 1.3  (bulk density)  kg ha-1

In Table 5 the following figures have been included:  ΔN (Table 4), N leached  (Table 3),  N uptake by crop,  mineralised N (equation [3]), EUF-Norg  and “b” values, corresponding to each yearly crop  in which N balance was monitored.

Table 5.- N mineralised in no fertilised plots during each crop, calculated from the N balance. Calibration of the  b coefficient relative to EUF-Norg.

| Year | aΔN (kg N ha-1) | bN Leached (kg N ha-1) | N uptake (kg N ha-1) | cMineralised N (kg N ha-1) | EUF-Norg (mg N 100g-1) | b |
| --- | --- | --- | --- | --- | --- | --- |
| 1999 | -32.5 | 3.2 | 102.6 | 73.3 | 2.50 | 29.3 |
| 2000 | -43.9 | 2.6 | 95.7 | 54.4 | 2.00 | 27.2 |
| 2001 | -23.5 | 1.6 | 82.4 | 60.5 | 1.82 | 33.2 |

a ΔN (see Table 4); bN leached (see Table 3); N uptake (Fig 2).

cMineralised N = ΔN + leached N + N uptake

“b” = N mineralised/ EUF-Norg

Discussion

The low concentrations of nitrate observed (Table 3) are justified by the soil characteristics, i.e., its shallowness and stoniness, which stimulate maize roots to extend into the whole soil volume above the limestone crust and practically remove all traces of nitrate.

The quantities (Table 5) of mineralised N were similar ( 73.3 kg N ha-1 in 1999, 54.4 kg N ha-1 in 2000 and 60.5 kg N ha-1 in 2001), indicating that N mineralisation is a characteristic of the soil in this weather conditions for a maize crop in this area. This is lower than what reported Sánchez et al. (1998) for a maize crop (160 kg ha-1) in a deep soil (2 m) and without stones. A comparison between both situations points out that the volume of soil involved in nitrogen mineralisation was lower in this case due to a rather shallow and stony soil, typical of this area.

Parameter ‘b’ [1 eq.] was recalculated from Nmin:  b = Nmin/EUF-Norg, which varied between 27.2 in 2000 and 33.2 in 2001 (Table 5). In 2000, available N was calculated using the ‘b’ value estimated from the previous year (b = 29.3, N available = 122 kg ha-1). An optimum dose of 150  kg N ha-1 was established, considering a efficiency for the nitrogen fertiliser of 70%, as estimated in previous experiments (Sánchez et al. 1998).  In 2001, the available N was estimated from the previous year’s N balance data for control plots (b = 27). The N dose for the optimised treatment (NO) was 130 kg N ha-1.

Some authors have found different “b” values depending on the growing season, geographical regions, climatology, management practices and types of soil (Table 6). In general, high “b” values can be identified in summer irrigated crops (maize) in hot climates (Sánchez et al. 1998). Cereals grown in winter (wheat) without irrigation give low “b” values (Steffens et al. 1990; Sánchez et al., 1998). Maize and sugar beet grown in Central Europe in summer without irrigation, give medium “b” values (Horn 1991; Wikicky et al. 1980). The case studied in the present work shows a “b” value near 30 (between 27.2 and 33.2), for the following combination of factors: a maize crop irrigated in summer, grown on a stony soil with a low depth. The results of this experiment  show that shallow irrigated soil must be included as one of the factors which affect  the “b” parameter. These calibrations of “b” parameter can be used in areas with the same irrigated crop and with similar weather conditions.

Table 6. Values of  “ b” parameter obtained by different authors in different crops.

| Authors | Crops | Soil | Country | Irrigation | Period | “b” |
| --- | --- | --- | --- | --- | --- | --- |
| Wiklicky et al (1981) | sugar beet | Loess | Austria | no | spring | 50 |
| Sánchez et al. (1998) | maize | Xerofluvent | Spain | yes | spring-summer | 85 |
| Sánchez et al. (1998) | winter wheat | Xerofluvent | Spain | no | winter | 32 |
| Horn (1990) | maize | Loess | Germany | no | spring | 47 |
| Steffens et al. (1990) | winter wheat | - | Germany | no | winter | 45 |

Fertilisation efficiency

Data for grain production and the N absorbed in each treatment during each year are shown in Fig. 2.  In 2000 there was a noticeable decrease of both the N absorbed and the grain production in the control plots (Table 7), due to a N deficit. In the same year, significant differences were observed (p<0.01) in the N absorbed between NO and NC treatments. However, this was not translated into differences in grain production, meaning that plants of the NC treated plots had a ‘luxury’ N absorption. In 2001 these results were repeated, i.e., there were no significant differences in grain production between NC and NO plots, despite the notable difference in N applied.

Table 7.- ANOVA for N uptake and grain yield among different treatments.

| ANOVA | Year | F | P | Duncan test |
| --- | --- | --- | --- | --- |
| N taken up | 2000 | 108.8 | 0.000 | C† (a) ‡, NO (b), NC(c) |
|  | 2001 | 65.3 | 0.0001 | C(a), NO (b), NC(c) |
| Grain yield | 2000 | 117.8 | 0.000 | C(a), NO (b), NC(b) |
|  | 2001 | 1410.0 | 0.000 | C(a), NO (b), NC(b) |

† C: control, NC: conventional nitrogen dosage,  and NO: optimised nitrogen.

‡  Different letters in brackets mean statistical difference between treatments at P<0.05.

Nitrogen fertiliser-use efficiency (NFUE) was determined for each treatment and each year (Garabet et al. 1998).

NFUE  = (N uptake in fertiliser plot– N uptake in control plot) /(applied N) x100		[5]

In the two years of experimentation (2000 and 2001) with N fertilisation, the NO treatment gave higher NFUE values (79.13 and 58.18 in 2000 and 2001, respectively) than the NC treatment (48.77 and 49.31 in 2000 and 2001, respectively). NFUE usually ranges from 40 to 70 with 80 as an upper limit (Greenwood and Draycott 1989).

These results show that optimised doses of N (NO) obtained taking the N mineralised into account  (“b” value) represents better NFUE than the conventional doses (NC) during the two experimental years.

### Conclusions

The methodology proposed in this paper, based on a N balance in no fertilised plots under field conditions, can determine the net mineralised N in shallow irrigated soils. The net N mineralised during crop growth was similar the  three years, but was smaller than in deeper soils.

Soil tests based on EUF methodology could be used to estimate available N. Parameter “b” in the Wiklicky and Németh equation was recalculated for shallow soils. It was near 30  (1 mg EUF-Norg-N 100g-1 soil = 30 kg N ha-1).

Optimised N rate of application (NO) led to a similar grain production as conventional rate (NC), despite the appreciable difference in the amount of N applied as fertiliser. However, significant differences in the absorbed N were recorded due to a ‘luxury’ absorption by plants in plots with conventional application. The optimisation of N fertilisation, based on the proposed determination of available N, reduces losses of N by leaching and improves the efficiency (NFUE) of applied fertilisers. As the N mineralised in the soil is low compared to the N uptake by the maize, it is frequent in this agroecosystem to fertilise with higher N rates than in deeper soils.

Acknowledgements

The authors are grateful to the Castilla La Mancha Regional Government and the FEDER program for funding (Project Nº 1FD97-0921-C02-01). Also, they wish to thank the Agroforestry Department of Castilla La Mancha University and Las Tiesas Experimental Field (Albacete) for their help in performing most of the fieldwork, and M.D. Atienza for laboratory assistance.

References

APPEL T., MENGEL K., 1998. Prediction of mineralizable nitrogen in soils on the basis of an analysis of extractable organic N. Z. Pflanzenernähr Bodenk 161: 433-452.

ARCARA P.G., GAMBA C., BIDINI D.,  MARCHETTI  R., 1999. The effect of urea and pig slurry fertilization on denitrification, direct nitrous oxide emission, volatile fatty acids, water-soluble carbon and anthrone-reactive carbon in maize-cropped soil from the Po plain ( Modena, Italy). Biol. Fért.  Soils  29: 270-276.

AOAC Official Methods of Analysis 1990. Helrich K Ed.  AOAC  Arlington VA.

BREMNER  J. M.,  1965. Methods Soils Anal.  Part 2, 1164.

BUSS P., 1993 The use of capacitance based measurements of real time soil water profile dynamics for irrigation scheduling. In: Under pressure. Irrig 93. Proc. Natl. Conf. Irrig. Assoc. Australia and the Ntl. Committee of Irrig. and Drainage, Launceston, Tasmania 1993. Irrig. Assoc. of Australia, Homebush, NSW.pp 17-19.

DÍEZ J.A., 1988. Revisión del método de determinación automatizado de nitrógeno UV oxidable en extractos de suelo. Anal.  Edafol.  Agrobiol.  46: 1028-1038.

DIEZ  J.A., CABALLERO R.,  BUSTOS A.,  ROMÁN  R., CARTAGENA  M.C., VALLEJO  A., 1996.  Control of nitrate pollution by application of controlled release fertilizer (CRF), compost and an optimized irrigation system. Fert.  Res.  43: 191-195.

DIEZ J.A., CABALLERO R., ROMÁN  R.,  TARQUIS  A., CARTAGENA  M.C., VALLEJO A., 2000.  Integrated Fertilizer and Irrigation Management to Reduce Nitrate Leaching in Central Spain. J. Environ.  Qual.   29: 1539-1547.

FÜRSTENFELD  F., NÉMETH  K., 1984.  EUF-N Fraktionen unter Güllebewirtschaftung und ihre Bedeutung für die Ernärhung der Zuckerrübe. Landwirtsch.  Forsch.  37: 175-187.

GARABET S., RYAN J., WOOD M., 1998. Nitrogen and water effects on wheat yield in a Mediterranean-type climate. II. Fertilizer-use efficency with labeled nitrogen. Field Crops Res. 58: 213-221

GREENWOOD D.J., DRAYCOTT A., 1989. Quantitative relationships for the dependence of growth rate of arable crops on their nitrogen content, dry weight and aerial environment. Plant Soil 91: 281-301.

HOUBA V.J.G., NOVOZAMSKY  I., HUYBREGTS A.W.M., VAN DER LEE J.J., 1986. Comparison of soil extractions by 0.01M Ca Cl2, by EUF and some conventional extraction procedures. Plant Soil 96: 433-437

HORN D., 1990.  Die Erstellung eines Stickstoffdüngungs-modells für Mais auf der Basis von Fieldversuchen und der Elektroultrafiltrations-methode. Ph D Thesis FB 17 Justus Liebig-Universität-Giessen.

ISO 10390,  1994.  Soil Quality. Determination of pH.

ISO 10693,  1995.  Soil Quality. Determination of carbonate content. Volumetric method.

ISO 14235,  1998.  Soil Quality. Determination of organic carbon by sulphochromic oxidation.

ISO 11277, 1998. Soil Quality. Determination of particle size distribution in mineral soil material. Method by sieving and sedimentation.

de JUAN J.A., TARJUELO J.M., VALIENTE M.,  GARCÍA  P.,  1996.  Model for optimal cropping patterns within the farm based on crop water production functions and irrigation uniformity. I Development of a decision model . Agric. Water  Manag.  31: 115-143.

KHAN S.A., MULVANEY R.L., HOEFT R.G., 2001. A simple soil test for detecting sites that are non-responsive to nitrogen fertilization. Soil Sci. Soc. Am. J. 65: 1751-1760.

MENGEL K., 1991. Available nitrogen in soils and its determination by the N min method and by electroultrafiltration (EUF). Fert. Res. 28: 251-262.

NÉMETH K.,  1979.  The availability of nutrients in the soil as determined by electroultrafiltration (EUF). Adv.  Agron.  31: 155-188.

PALTINEANU  C., STARR  J. L., 1997.  Real-time soil water dynamics using multisensor capacitance probes: Laboratory calibration. Soil Sci.  Soc.  Am.  J.  61: 1576-1585.

POLETSCHNY H., FABIAN M., 1989. Vergleichende Erprobung verschiedener Stickstoffbestimmungsmethoden in Böden. Schriftenr Bundesminist Ernaehr, Landwirsch. Forsten  Reihe A.  Anew  Wiss  378.

ROMÁN R., CABALLERO R., BUSTOS A., DIEZ J.A., CARTAGENA M.C., VALLEJO A., CABALLERO A., 1996. Water and solutes movement under conventional corn in Central Spain. I. Water balance. Soil Sci. Soc. Am. J. 60 : 1530-1536.

SANCHEZ  L., DIEZ  J.A.,  VALLEJO  A.,  CARTAGENA  M.C.,  POLO  A., 1998.  Estimate of mineralized organic nitrogen in soils using nitrogen balances and determining available nitrogen by the electroultrafiltration technique. Application to Mediterranean climate soils. J. Agric.  Food  Chem.  46:  2036-2043.

SÁNCHEZ L., DÍEZ J.A., VALLEJO A., CARTAGENA M.C., 2001. Denitrification losses from irrigated crops in Central Spain. Soil Biol. Biochem. 33: 1201-1209.

SENTEK 2000. Enviroscam manual 1999-2000. Sentek Pty Ltd, Enviroscam 4.1. www.sentek.com.au

STANFORD G., 1982 Assessment of soil nitrogen availability. In: F.J. Stevenson et al. (ed.) Nitrogen in agricultural soils. Agron. Monogr. 22. ASA, CSSA, and SSSA, Madison , WI, pp. 651-658.

STEFFENS  D., BAREKZAI A.,  BOHRING  J., POOS F., 1990. Die EUF-löslichen Stickstoffgehalte in Ackerböden des Landkreises Giessen. Agrobiol.  Res.  43:  319-329.

WIKLICKY  L., NÉMETH  K., 1981.   Düngungsoptimierung mittels EUF-Bodenuntersuchung bei der Zuckerrübe. Sonderdruck aus Band  106:  982-998.

WIKLICKY L.,  NÉMETH  K.,  RECKE  H.,  1983.  Beurteilung des Stickstoff-Düngebedarfs für die Zuckerrübe mittels EUF. In Simposium “Stickstoff und Zuckerrübe” Intern  Institut für Zuckerrübenforschung  Brussels,   533-543.

ZIEGLER  K., NÉMETH  K.,  MENGEL,  K.,  1992.   Relationships between electroultrafiltration (EUF) extractable nitrogen, grain yield, and optimum nitrogen fertilizer rates for winter wheat. Fert.  Res.   32: 37-43.

Fig 1

.

Fig 2

Figure caption:

Figure 1. Equipment installed in plots

Figure 2. N uptake and grain yield with different treatments and error bars.